## Slide 1
EdgeMATX
Design and Integration of a TinyML Systolic Accelerator with PicoRV32
Submitted by
Nishchay Pallav 221EC233
Mohammad Omar Sulemani 221EC230
Md Atib Kaif 221EC129
Under the Guidance of Dr Rathamala Rao
Dept. of Electronics & Communication Engineering National Institute of Technology Karnataka, Surathkal — 575025
673
Cycles
54×
Peak Speedup
19/19
Tests Pass
4×4
Systolic Array

## Slide 2
The Problem
Matrix multiplication is ubiquitous — and painfully slow on embedded CPUs
EdgeMATX · NITK Surathkal · ECE Department · 2026
Where It's Needed
⚡ TinyML Inference
Neural network layers are dense GEMM ops
📡 Digital Signal Processing
Convolution = repeated matrix multiply
🔬 Scientific Computing
Linear solvers, transforms — all matrix ops
📷 Image Processing
Filters, transforms, feature extraction
Sequential CPU Execution
for i in range(4):
for j in range(4):
for k in range(4):
C[i][j] += A[i][k]
* B[k][j]
64 multiply-accumulate ops
executed one at a time
RV32I (no MUL): 26,130 cycles
RV32IM (with MUL): 7,975 cycles
The Gap
26 K
cycles wasted per 4×4 multiply
100%
sequential execution on CPU
0×
hardware parallelism

## Slide 3
The Solution: EdgeMATX
A custom PCPI coprocessor tightly coupled to PicoRV32
EdgeMATX · NITK Surathkal · ECE Department · 2026
One custom instruction replaces 64 sequential CPU operations
⚡ Tightly Coupled
PCPI interface: zero memory-mapped overhead. CPU stalls and resumes — no interrupts, no DMA.
🔲 Systolic Datapath
4×4 array of 16 processing elements. All 16 MACs execute in parallel every clock cycle.
🔢 Q5.10 Fixed-Point
16-bit signed arithmetic. No floating-point hardware needed — ideal for constrained silicon.
673
Deterministic cycles
38.83×
Speedup (sparse data)
53.86×
Speedup (dense data)
11.85×
Speedup vs MUL-equipped rv32im

## Slide 4
System Architecture
PicoRV32 + PCPI custom instruction interface + 4×4 systolic accelerator
EdgeMATX · NITK Surathkal · ECE Department · 2026
Firmware Layer (RISC-V C code)
Load matrix A → 0x100–0x13C
Load matrix B → 0x140–0x17C
Execute custom instruction 0x5420818b
Read result C ← 0x200–0x23C
→
PicoRV32 CPU Core
RV32I ISA
ENABLE_PCPI=1
ENABLE_MUL=0
Custom opcode decoded & dispatched via PCPI signals
Stalls until pcpi_ready=1
PCPI
⟷
PCPI Coprocessor Wrapper
Detects custom opcode
Drives matrix engine
Issues pcpi_ready
4×4 Systolic Array
16 Processing Elements Q5.10 Fixed-Point MACs Output-Stationary Dataflow
↕ Memory
Memory Map
0x100–0x13C
Matrix A (in)
0x140–0x17C
Matrix B (in)
0x200–0x23C
Matrix C (out)
↔

## Slide 5
PCPI: The Custom Instruction Bridge
Pico Co-Processor Interface — zero-cost hardware dispatch
EdgeMATX · NITK Surathkal · ECE Department · 2026
Interface Signals
▸ pcpi_valid
CPU → CoPro · Custom instruction detected
▸ pcpi_insn
CPU → CoPro · Full 32-bit instruction word
▸ pcpi_rs1
CPU → CoPro · Source register rs1 (matrix A addr)
▸ pcpi_rs2
CPU → CoPro · Source register rs2 (matrix B addr)
▸ pcpi_wr
CoPro → CPU · Write result back to rd
▸ pcpi_rd
CoPro → CPU · Result value (unused in EdgeMATX)
▸ pcpi_ready
CoPro → CPU · Computation done — CPU resumes
▸ pcpi_wait
CoPro → CPU · Hold CPU stall (optional)
Execution Handshake
1
CPU fetches custom instruction 0x5420818b
2
pcpi_valid=1, instruction + rs1/rs2 broadcast
3
CPU stalls — waiting for pcpi_ready
4
Coprocessor reads matrix A & B from memory
5
4×4 systolic array computes all 16 dot products
6
Results written to matrix C region (0x200–0x23C)
7
pcpi_ready=1 → CPU resumes next instruction
Custom opcode: 0x5420818b (custom-0 space, opcode 0001011)

## Slide 6
The 4×4 Systolic Array
16 parallel Processing Elements — output-stationary dataflow
EdgeMATX · NITK Surathkal · ECE Department · 2026
B col 0
↓
B col 1
↓
B col 2
↓
B col 3
↓
A row 0 →
PE [0,0]
MAC
→
↓
PE [0,1]
MAC
→
↓
PE [0,2]
MAC
→
↓
PE [0,3]
MAC
↓
→ C row 0
A row 1 →
PE [1,0]
MAC
→
↓
PE [1,1]
MAC
→
↓
PE [1,2]
MAC
→
↓
PE [1,3]
MAC
↓
→ C row 1
A row 2 →
PE [2,0]
MAC
→
↓
PE [2,1]
MAC
→
↓
PE [2,2]
MAC
→
↓
PE [2,3]
MAC
↓
→ C row 2
A row 3 →
PE [3,0]
MAC
→
PE [3,1]
MAC
→
PE [3,2]
MAC
→
PE [3,3]
MAC
→ C row 3
How It Works
▸ Output-stationary
Each PE accumulates its partial sum for C[i,j] in place
▸ Row broadcast
Row i of matrix A flows right across row i of PEs
▸ Column broadcast
Column j of matrix B flows down column j of PEs
▸ Parallel MACs
All 16 PEs execute simultaneously every clock cycle
▸ Deterministic
673 cycles regardless of operand values
▸ 16-bit Q5.10
Multiply → shift-right 10 → accumulate → truncate

## Slide 7
Q5.10 Fixed-Point Arithmetic
16-bit two's complement — integer simplicity, fractional precision
EdgeMATX · NITK Surathkal · ECE Department · 2026
S
15
I4
14
I3
13
I2
12
I1
11
I0
10
F9
9
F8
8
F7
7
F6
6
F5
5
F4
4
F3
3
F2
2
F1
1
F0
0
Sign (1 bit)
Integer part (5 bits)
Fractional part (10 bits)
Range
−32.0 to +31.999
Resolution
1 / 1024 ≈ 0.001
Format
16-bit signed integer
Scaling
Multiply → shift right 10 bits
Processing Element MAC Operation (per clock cycle):
① Multiply
a_in × b_in → 32-bit signed product
② Scale
product >>> 10 (arithmetic right-shift corrects Q5.10 format)
③ Accumulate
acc += scaled_product (32-bit running sum)
④ Pass through
a_out ← a_in ; b_out ← b_in (feed neighbours)

## Slide 8
Verification Strategy
Four-layer simulation campaign — from unit tests to full system benchmarking
EdgeMATX · NITK Surathkal · ECE Department · 2026
4
Layer 4 · Performance Benchmarking
Cycle-count measurement against two software baselines (no-MUL and MUL-equipped).
673 cycles measured
3
Layer 3 · Protocol Handoff Validation
Isolated test of PCPI signal handshake — pcpi_valid, pcpi_ready, pcpi_insn correctness.
PASS
2
Layer 2 · CPU Integration Regression
Full system simulation: PicoRV32 + PCPI wrapper + accelerator. 8 input profiles.
8 / 8 PASS
1
Layer 1 · Standalone Unit Tests
Accelerator module in isolation. Zero, identity, dense, boundary, negative-element cases.
19 / 19 PASS

## Slide 9
Verification Results
100% pass rate across all test flows — simulation-complete milestone
EdgeMATX · NITK Surathkal · ECE Department · 2026
100%
PASS RATE
19 / 19 standalone unit tests
8 / 8 integration cases
5 / 5 professor demo cases
✓ handoff protocol test
✓ one-command gate check
Test Category Breakdown
Zero / Null Matrix
2/2
Identity Matrix
3/3
Dense (varied magnitudes)
8/8
Q5.10 Sign Boundary
4/4
Negative Elements
2/2
Integration: varied inputs
8/8
Professor Demo Cases
5/5

## Slide 10
Performance: Cycle Counts
Deterministic execution — 673 cycles regardless of input values
EdgeMATX · NITK Surathkal · ECE Department · 2026
673
EdgeMATX Accelerator
rv32i + PCPI
7,975
Software + MUL
rv32im baseline
26,130
Software (no MUL)
rv32i baseline
36,246
Software (no MUL, dense)
dense profile
Chart: Cycle Count Comparison
| EdgeMATX (PCPI) | SW + MUL (rv32im) | SW no-MUL (rv32i) | SW no-MUL (dense)
Cycles | 673 | 7975 | 26130 | 36246

## Slide 11
Performance: Speedup
38–54× over rv32i software baseline — 11.85× over MUL-equipped core
EdgeMATX · NITK Surathkal · ECE Department · 2026
38.83×
Sparse vs rv32i
Identity-sequence benchmark 26,130 → 673 cycles
53.86×
Dense vs rv32i
Live dense profile 36,246 → 673 cycles
11.85×
Any vs rv32im
Even against MUL-equipped core 7,975 → 673 cycles
Consolidated Speedup Table
Profile
EdgeMATX
SW (no MUL)
SW (MUL)
Speedup vs no-MUL
Speedup vs MUL
identity_x_sequence
673
26,130
7,975
38.83×
11.85×
live_real_input (dense)
673
36,246
7,975
53.86×
11.85×

## Slide 12
Interactive Visualizers
Explore the design live in your browser
EdgeMATX · NITK Surathkal · ECE Department · 2026
Architecture Overview
🔗 riscv-visualizer-2.vercel.app
▸ High-level system architecture and dataflow
▸ Firmware layer · PicoRV32 · PCPI · Systolic Array
▸ Step-through execution with annotations
[ Open in browser to view live simulation ]
Processor Signal Simulation
🔗 tinyml-pcpi-visualizer.vercel.app
▸ Instruction decode · PCPI signal timeline
▸ Accelerator invocation waveform
▸ Systolic array computation state
[ Open in browser to view live simulation ]

## Slide 13
What's Next: Pynq-Z2 FPGA Deployment
Simulation-proven design → physical hardware closure
EdgeMATX · NITK Surathkal · ECE Department · 2026
✅ DONE
Simulation
673-cycle verified behaviour on Icarus Verilog
→
🔜 NEXT
FPGA Synthesis
Map to Pynq-Z2 Xilinx Zynq-7020 Post-synthesis timing
→
🔭 FUTURE
Scale & Deploy
On-board cycle counts AXI/BRAM memory 8×8 array extension
Open Items Before Hardware Closure
▸ Cycle-scaling estimator anchor needs updating (869 → 673 cycles)
▸ On-board rdcycle CSR measurements to cross-validate simulation results
▸ AXI-BRAM memory interface replacing software-driven memory reads

## Slide 14
Conclusion
Simulation-complete milestone — all objectives achieved
EdgeMATX · NITK Surathkal · ECE Department · 2026
Hardware Accelerator
4×4 systolic array with 16 Q5.10 fixed-point MACs, implemented in Verilog
CPU Integration
Tightly coupled to PicoRV32 via PCPI custom instruction — single opcode dispatch
Deterministic Execution
673-cycle latency, invariant to operand values — ideal for real-time systems
Verified Performance
38.83× – 53.86× speedup over rv32i; 11.85× over MUL-equipped rv32im
100% Test Coverage
19/19 standalone · 8/8 integration · 5/5 professor demo · handoff PASS
Interactive Tooling
Two live web visualizers for architecture walkthrough and signal-level simulation

## Slide 15
Thank You
Questions & Discussion
Team
Nishchay Pallav 221EC233
Mohammad Omar Sulemani 221EC230
Md Atib Kaif 221EC129
Live Visualizers
🔗 riscv-visualizer-2.vercel.app
🔗 tinyml-pcpi-visualizer.vercel.app
Dept. of Electronics & Communication Engineering National Institute of Technology Karnataka, Surathkal — 575025 · 2026